## Slide 1
WiFi-Display
Notes: <number>

## Slide 2
WFD介绍
Wifi Display中分为Source和Sink两种角色
Source是用于encode并输出TS流
Sink用于decode并显示TS流

## Slide 3
WFD连接
Wifi Display连接过程的建立，包含P2P的部分和RTSP的部分
连接的时候先建立P2p连接，后连接RTSP
断开的时候，先断开RTSP，后断开P2p
与wifi direct连接过程类似，但WFD协议有其特有的IE, 在打开wifi阶段，wifi在初始化的时侯会首先将WFD的功能disable掉，这样在发送的帧里面都不会带WFD的IE，在Enable WFD之后会带WFD的IE信息
WFD的P2P连接过程，默认intent为0，尽可能使手机作为GC。

## Slide 4
P2p连接
Scan：全信道的扫描。
Find：search和listen的循环，在3个channel（1，6，11）上扫描，在1 个 channel（1，6，11中的一个）上听。
Formation:包括了go neg （协商谁是go）过程和provison（协商使双方具有相同的配置）过程。
Operation: auth，assoc，4-way handshake，2-way handshake

## Slide 5
P2p连接过程
第一项是GO negotiation, 第三项称为Provision， 前三项合起来称为P2P Group Formation
GO Negotiation过程
GO端初始化，GC端扫描并连接GO
WSC的过程，GO分配证书给GC
断开连接后，GC再通过4次握手连接GO

## Slide 6
RTSP连接
RTSP连接过程，手机端首先设置一个监听CONTROL PORT，listen指定的IP和端口上面的TCP连接请求, 最后会设置Rtsp连接请求的timeout，当用于Miracast认证时间是120秒，正常的使用中是30秒，如果在这么长的时间内没有收到Sink的TCP请求，则表示失败了
RTSP 连接过程，Dongle充当Server的角色，会主动发起RTSP连接。
RTSP（Real Time Streaming Protocol），实时流传输协议

## Slide 7
P2P的完整连接流程

## Slide 8
Search
WifiDisplayController中下搜索命令，搜索时间是120S
WifiDisplayController: requestStartScan
WifiHW : enter -->wifi_send_command cmd=P2P_FIND 120
Probe Request ，扫描设备，也让对方发现我们, 在scan时会把我们的listen channel带出去，让对方知道我们会在哪个信道上听
wpa_supplicant: P2P: Starting search
wpa_supplicant: WPS: Building WPS IE for Probe Request
wpa_supplicant: WPS: * Config Methods (4388)
wpa_supplicant: P2P: * Listen Channel: Regulatory Class 81 Channel 6

## Slide 9
Search Result
搜到设备,括号中的内容代表我们扫描到的p2p设备的个数，IE携带对方的设备信息。
wpa_supplicant: P2P: Scan results received (1 BSS)
wpa_supplicant: P2P: Parsing WPS IE
wpa_supplicant: P2P: Config Methods (WPS): 0x188
wpa_supplicant: P2P: * Device Info: addr 02:25:26:37:46:0a primary device type 1-0050F204-5 device name 'V102-37460A' config methods 0x188
wpa_supplicant: P2P-DEVICE-FOUND 02:25:26:37:46:0a p2p_dev_addr=02:25:26:37:46:0a pri_dev_type=1-0050F204-5 name='V102-37460A' config_methods=0x188 dev_capab=0x20 group_capab=0x8 wfd_dev_info=0x00000601191c44012c
WifiMonitor收到这样的event后，会将P2P-DEVICE-FOUND后面的data数据封装成为一个WifiP2pDevice对象

## Slide 10
如何区分device设备
如何区分device设备？
wpa_supplicant: P2P-DEVICE-FOUND 02:25:26:37:46:0a p2p_dev_addr=02:25:26:37:46:0a pri_dev_type=1-0050F204-5 name='V102-37460A' config_methods=0x188 dev_capab=0x20 group_capab=0x8 wfd_dev_info=0x00000601191c44012c
private static boolean isWifiDisplay(WifiP2pDevice device) {
return device.wfdInfo != null
&& device.wfdInfo.isWfdEnabled()
&& device.wfdInfo.isSessionAvailable() ///Add by MTK
&& isPrimarySinkDeviceType(device.wfdInfo.getDeviceType());
}
private static boolean isPrimarySinkDeviceType(int deviceType) {
return deviceType == WifiP2pWfdInfo.PRIMARY_SINK
|| deviceType == WifiP2pWfdInfo.SOURCE_OR_PRIMARY_SINK;
}

## Slide 11
WFD跟Wifi-Direct连接方式的区别
Wifi Direct的连接方式有两种：”persistent” 和 ”非persistent”。
跟wifi Direct一样，Android默认的情况下WFD也是支持这两种方式的连接，但是跟部分dongle连接过程中出现高频率fail的问题（V102, netgear），MTK为了改善跟dongle的兼容性而屏蔽了“persistent”的连接方式，所以目前WFD只有“非persistent”方式。

## Slide 12
Request Connect
Request Connect
WifiDisplayController: requestConnect, address = 02:25:26:37:46:0a
WifiDisplayController: Initiated connection to Wifi display: V102-37460A
启动RTSP监听
WifiDisplayController: Listening for RTSP connection on 127.0.0.1:7236 from Wifi display: V102-37460A , Speed-Up rtsp setup, DRM Content isPlaying = false

## Slide 13
Provision Discovery Request
连接P2p，首先发PD request，协商连接信息，如PBC/display/keypad,携带的信息取决于config信息,这帧中0x80代表对方wps的方式是pbc，目的是想让对方知道我们的wps方式。
wpa_supplicant: p2p0: Control interface command 'P2P_PROV_DISC 02:25:26:37:46:0a pbc‘
wpa_supplicant: P2P: Provision Discovery Request with 02:25:26:37:46:0a (config methods 0x80)
确认发送成功
wpa_supplicant: P2P: Provision Discovery Request TX callback: success=1

## Slide 14
Provison Discover Resp
接收到对方的回复，携带对方的连接方式信息：PBC（0X80）
wpa_supplicant: P2P: Received Provision Discovery Response from 02:25:26:37:46:0a with config methods 0x80

## Slide 15
GO Neg Request
GO Neg Request
wpa_supplicant: P2P: Request to start group negotiation - peer=02:25:26:37:46:0a GO Intent=0 Intended Interface Address=46:46:43:32:31:ab wps_method=3 persistent_group=2 pd_before_go_neg=0
wpa_supplicant: P2P: Sending GO Negotiation Request
注意我们携带的Intent 0, Tie breaker 1
wpa_supplicant: P2P: * GO Intent: Intent 0 Tie breaker 1
成功发送GO neg Req，在发送的channel上定时500ms等待对方回复go neg resp。如果0.5ms等待不到就超时
pa_supplicant: P2P: GO Negotiation Request TX callback: success=1，
wpa_supplicant: P2P: Set timeout (state=CONNECT): 0.500000 sec

## Slide 16
GO Neg Response
收到对方回的go neg response，清掉timer，解析到对方的status为0代表成功
wpa_supplicant: P2P: Received GO Negotiation Response from 02:25:26:37:46:0a (freq=2412)
wpa_supplicant: P2P: * Status: 0
对方回复的Intent和Tie breaker信息，用于确定谁是GO。
wpa_supplicant: P2P: * GO Intent: Intent 14 Tie breaker 0
协商谁是GO，首先看Intent，谁大谁是GO，如果Intent相同，Tie Breaker=1的是GO，如果双方都是15，则协商不成功，说明双方都只想做go，谈判破裂；否则谁的intent大，谁就当go；如果双方的intent相等，则谁的tie breaker为1，谁就当go（协议保证了tie breaker是不同的）。

## Slide 17
Go协商过程WFD跟P2P的区别
如果是wifi direct连接，那么在Go过程对方会回复失败，意思是等对方ready后，再主动连我们，Status为1就表示失败。对方回失败主要是为了实现被邀请的一方可以选择“接受”和“拒绝”的功能。具体过程是这样：如果被邀请方点的是“接受”，在回复了失败以后，被邀请方会再发go neg req来开始go neg的过程；如果被邀请方点的是“拒绝”，在回复了失败以后，被邀请方就不会再发go neg req来开始go neg的过程，而邀请方因为一直等不到对方发邀请，所以最后超时。
在WFD中不需要对方选择拒绝或者接受，默认都是要连接的，直接回复Status：0， 代表成功

## Slide 18
GO协商结果
Go协商过程确定channel
wpa_supplicant: P2P: * Operating Channel: Regulatory Class 115 Channel 36
确定谁是GO
wpa_supplicant: P2P: GO Negotiation with 02:25:26:37:46:0a completed (peer will be GO)
GO成功的标志（P2P-GO-NEG-SUCCESS ）
wpa_supplicant: P2P-GO-NEG-SUCCESS role=client freq=5180 ht40=0 peer_dev=02:25:26:37:46:0a peer_iface=02:25:26:37:46:0a wps_method=PBC

## Slide 19
provison
Go neg 过程解决了谁是go的问题，但是没有解决让双方配置成相同密码的问题。这个过程在wifi direct的spec里叫做provison。provisoning过程，完成让双方有相同的配置。这个过程与wps连接的过程类似, 是在wps之前进行的，主要协商是否有相同的wps支持能力，当然也有其他作用。由于provison在log里面并不明显，我们不贴log了。

## Slide 20
wps
扫描并连上了go 之后，然后进行wps协商配置，M1~M8完整的wps过程，让两方具有相同的配置。
wpa_supplicant: EAP-WSC: WAIT_START -> MESG
wpa_supplicant: WPS: Building Message M1
wpa_supplicant: WPS: Received M2
wpa_supplicant: WPS: Building Message M3
wpa_supplicant: WPS: Received M4
wpa_supplicant: WPS: Building Message M5
wpa_supplicant: WPS: Received M6
wpa_supplicant: WPS: Building Message M7
wpa_supplicant: WPS: Received M8
wpa_supplicant: WPS: Building Message WSC_Done
wpa_supplicant: p2p0: WPS-SUCCESS

## Slide 21
Formation
Formation是wifi direct spec里的述语，它代表2个过程：go neg过程和provision过程。
wpa_supplicant: P2P-GROUP-FORMATION-SUCCESS

## Slide 22
Disconnect
按spec的规定，在wps完成以后，go会让gc断开，重新以刚刚配置好的安全方式连接，所以在wps的最后会以eap failure达到这个目的，请注意，以下这些fail信息都是正常的。
wpa_supplicant: EAP: Received EAP-Failure
wpa_supplicant: p2p0: CTRL-EVENT-EAP-FAILURE EAP authentication failed
wpa_supplicant: p2p0: Request to deauthenticate - bssid=02:25:26:37:46:0a pending_bssid=00:00:00:00:00:00 reason=3 state=ASSOCIATED
wpa_supplicant: p2p0: Event DEAUTH (12) received
wpa_supplicant: p2p0: Deauthentication notification
wpa_supplicant: p2p0: CTRL-EVENT-DISCONNECTED bssid=02:25:26:37:46:0a reason=3 locally_generated=1

## Slide 23
4-way handshake
Gc断开重新关联上。经过wps过程，gc了解到go的链接方式，密码，所以后面会直接进行4次握手,生成通信密钥。
开始四次握手
wpa_supplicant: p2p0: State: ASSOCIATED -> 4WAY_HANDSHAKE
go发送1/4次握手，把Go方的随机数发给GC
wpa_supplicant: p2p0: WPA: RX message 1 of 4-Way Handshake from 02:25:26:37:46:0a (ver=2)
GO收到gc的2/4握手，算出ptk（加密单播包用的）。
wpa_supplicant: p2p0: WPA: Sending EAPOL-Key 2/4
GO发3/4握手，将算好的gtk（加密组播密钥）发给gc。
wpa_supplicant: p2p0: WPA: RX message 3 of 4-Way Handshake from 02:25:26:37:46:0a (ver=2)
Gc发4/4握手确认收到。
wpa_supplicant: p2p0: WPA: Sending EAPOL-Key 4/4
到此go与gc连接成功。
wpa_supplicant: p2p0: State: 4WAY_HANDSHAKE -> GROUP_HANDSHAKE

## Slide 24
2-way handshake
wpa_supplicant: p2p0: State: 4WAY_HANDSHAKE -> GROUP_HANDSHAKE
wpa_supplicant: RSN: received GTK in pairwise handshake - hexdump(len=18): [REMOVED]
wpa_supplicant: WPA: Group Key - hexdump(len=16): [REMOVED]
wpa_supplicant: p2p0: WPA: Installing GTK to the driver (keyidx=1 tx=0 len=16)
wpa_supplicant: broadcast key
wpa_supplicant: p2p0: WPA: Key negotiation completed with 02:25:26:37:46:0a [PTK=CCMP GTK=CCMP]
wpa_supplicant: p2p0: State: GROUP_HANDSHAKE -> COMPLETED

## Slide 25
WFD Connected
P2p连接完成
wpa_supplicant: p2p0: CTRL-EVENT-CONNECTED - Connection to 02:25:26:37:46:0a completed (auth) [id=0 id_str=]
P2p成功连接之后开始RTSP连接
WifiDisplayController: Connected to Wifi display: V102-37460A
WifiDisplayController: Opened RTSP connection with Wifi display: V102-37460A
WFD成功的标志（ actionAtConnected ）
WifiDisplayController: actionAtConnected

## Slide 26
断开请求
用户手动断开
WifiDisplayController: requestDisconnect
先断开RTSP
WifiDisplayController: Stopped listening for RTSP connection on 127.0.0.1:7236 from Wifi display : V102-37460A
WifiDisplayController: before dispose() --->
WifiDisplayController: <--- after dispose()
断开P2P的时候，直接removegroup
WifiP2pService: GroupCreatedState remove group
wpa_supplicant: p2p0: Control interface command 'P2P_GROUP_REMOVE p2p0‘
wpa_supplicant: p2p0: CTRL-EVENT-DISCONNECTED bssid=02:25:26:37:46:0a reason=3 locally_generated=1
WifiDisplayController检测到断开,会去更新UI
WifiDisplayController: actionAtDisconnected

## Slide 27
Thanks！